## Slide 1
Implementing MLFFs/MLIPs on Molten Cu-In Nanoparticle Systems to Model Growth of Carbon Nanotubes
Anmol Bansal
Sourish Das
Shreshth Gupta
Supervised by: Dr. Vishal Agarwal Department of Chemical Engineering IIT Kanpur

## Slide 2
Part 1: Introduction to Machine-Learned Force Fields (MLFFs) / Interatomic Potentials (MLIPs)

## Slide 3
What are MLFFs/MLIPs?
Introduction
Atomic configurations → Potential Energy Surface
Input: Coordinates/vectors + element types Output: Spatial derivatives of PES
Atomistic Simulations: - AIMD - PBP
MLIPs are the Bridge!

## Slide 4
What are MLFFs/MLIPs?
Motivation and Need
Computational infeasibility of AIMD in large chemical systems and longer timescales.
Less accuracy of PBP-based MD for materials.
MLIPs can be supplemented with physics functionals for extrapolating complicated energy profiles.
MLIPs: Best of Both Worlds.
Training Dataset (AIMD)
Physical Parameters (PBP)
Machine Learned Interatomic Potential

## Slide 5
What are MLFFs/MLIPs?
Basic Principles
Atomic Environment Featurization
Descriptors
Symmetrical Invariance
Unification of Explicit and Implicit AEF

## Slide 6
Part 2: Scope of Study & Literature Review on Applied MLFFs

## Slide 7
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Traditional MLIP training paradigms ill-equipped to handle rare events.
Workflow: - Automated Reaction Exploration - Uncertainty Driven Active Learning - Transition State Sampling
Benchmarking: - Gas Phase - Solution Phase - Heterogeneous

## Slide 8
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning

## Slide 9
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Methodology: - Initial molecules for bootstrap dataset. - Short AIMD - MLIP training - Configuration filtering
Committee of MLIPs: - Product prediction from reactant SMILES. - TS/Intermediates setup through SE-GSM and/or NEB. - MLIP driven reaction exploration.

## Slide 10
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Uncatalyzed Gas-Phase Ammonia Synthesis
Reactions: - N2 + H2 → cis− HNNH - cis− HNNH + H2 → H2NNH2 - H2NNH2 + H2 → HNNH3 + H2 - HNNH3+H2 → NH3+NH3.
Both NSC-RAL and SC-RAL MLIPs show significant errors in predicting the forward and reverse barriers, indicating poor performance in estimating the transition state energy.

## Slide 11
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Hydrolysis of Methanamine
Reactions: - CH2NH + H2O → NH2CH2OH - NH2CH2OH → NH2CH2OH - NH2CH2OH → CH2O + NH3
Both MLIPs predict similar reaction PES as well as forward and reverse barriers. Although the absolute error is small for this reaction, the reaction barrier itself is very low, which may result in large a percentage error.

## Slide 12
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Snapshots of TixCy surfaces before (t = 0 ps) and after (t = 500 ps) T = 1200 K NVT-MD simulations initialized with 20 CH4 molecules. Ti atoms shown in light gray, C in dark gray, H in white.
Methane Activation and C−C Coupling Surface Catalysis Reaction on Titanium Carbide

## Slide 13
Literature on MLFFs – Molten Systems, Nanomaterials, CNT Growth, etc.
Reactive Active Learning
Snapshots of TixCy surfaces before (t = 0 ps) and after (t = 500 ps) T = 1200 K NVT-MD simulations initialized with 20 CH4 molecules. Ti atoms shown in light gray, C in dark gray, H in white.
Methane Activation and C−C Coupling Surface Catalysis Reaction on Titanium Carbide

## Slide 14
Implementation Toolkit
DeePMD-kit
Deep neural networks for MD.
Local reference frame and local environment assigned to each atom.
Bypassing auxiliary quantities for preserving symmetries.
Flexible family of loss functions.
Computational cost scales linearly with the number of atoms.
Can be parallelized due to local decomposition and the near-neighbor dependence of its “atomic energies”.

## Slide 15
DeePMD-kit
Local coordinate frame (Dij) is set up for every atom a neighbors inside Rc. This preserves translational, rotational, and permutational symmetries. Dij contains radial and angular information of neighbouring atom.
Dij is the FF-DNN input. A linear transformation is applied to the input data, followed by activation with hyperbolic tangent function. There are three hidden layers in our network. We use SGD with the Adam optimizer.
Implementation Toolkit

## Slide 16
DeePMD-kit
Implementation Toolkit

## Slide 17
DeePMD-kit
Implementation Toolkit

## Slide 18
DeePMD-kit
Implementation Toolkit

## Slide 19
Part 3: Method Developing MLFF for a specific chemical system

## Slide 20
Types of Data
Anmol & Sourish

## Slide 21
Data Generation
Anmol

## Slide 22
Using exploration-exploitation phase of AL-NEB.
Collecting data points at regions of most uncertainty.
No need for renunciation phase.
Avoiding seeds from unnecessary regions.
R [Initial Point]
P [Final Point]
Reactive Pathway
Idea of an “ALNEB-guided Swarm AIMD”

## Slide 23
R [Initial Point]
P [Final Point]
Seeds lying along the transition manifold (Reactive Pathway)
Idea of an “ALNEB-guided Swarm AIMD”

## Slide 24
Idea of an “ALNEB-guided Swarm AIMD”
R [Initial Point]
P [Final Point]
Short AIMD trajectories running with different initial velocity states covering the configurations around the seeds like a swarm.
All seeds from the ALNEB run are used and data from the transition manifold is covered.

## Slide 25
How does ALNEB work in our favour?
Active learning framework using GPR.
Constructs surrogate PES.
Selects training points in two phases.
Reduces expensive QM evaluations.

## Slide 26
How does ALNEB work in our favour?

## Slide 27
Descriptor Space Visualisation of a Toy Dataset: CH4  CH3 + H
Generated by random perturbations of the CH4 bonds.
psi4 based DFT labelling.

## Slide 28
Descriptor Space Visualisation of a Toy Dataset: CH4  CH3 + H
Generated by random perturbations of the CH4 bonds.
psi4 based DFT labelling.
CH4 cluster
CH3 cluster
Transition manifold (irrespective of the presence of a defined TS)

## Slide 29
Descriptor Space Visualisation of the Training Dataset: DeepCNT-22

## Slide 30
Data Processing: Farthest Point Sampling

## Slide 31
MLFF Model Ensemble Training

## Slide 32
Implementation of Delta Learning in MLIP Development
Anmol

## Slide 33
Development Milestones
Toy Problem: HCN  HNC Isomerisation.
  Randomly generated data + single-pass training
  ALNEB seed data + single-pass training
  ALNEB seed data + AL loop training
  ALNEB guided swarm AIMD data + single-pass training
  ALNEB guided swarm AIMD data + AL loop training
  Generalisation and HPC-compatible script preparation
Toy Problem: CH4  CH3 + H
  Similar milestones as the HCN toy problem
Result Benchmarking: GAP-20
Result Benchmarking: DeepCNT-22
Production: Pure Metal + Alloy (Cu-In) MLIP
Production: CNT Growth on Molten Alloy Nanoparticle MLIP
Anmol

## Slide 34
Part 4:
Toy Problems HCN  HNC Isomerisation
CH4 Dissociation

## Slide 35
Generated by random perturbations of the HCN bonds.
psi4 based DFT labelling.
Toy Problem: HCN  HNC Isomerisation

## Slide 36
Toy Problem: HCN  HNC Isomerisation

## Slide 37
Toy Problem: HCN  HNC Isomerisation

## Slide 38
Toy Problem: HCN  HNC Isomerisation
Learning Curves & RMSE values

## Slide 39
Toy Problem: HCN  HNC Isomerisation
Energy Parity Plots: Training and Validation

## Slide 40
Toy Problem: HCN  HNC Isomerisation
Force Parity Plots: Training and Validation

## Slide 41
Toy Problem: HCN  HNC Isomerisation
Committee Uncertainty Histogram

## Slide 42
Toy Problem: HCN  HNC Isomerisation
Parity Plots: Testing

## Slide 43
Toy Problem: HCN  HNC Isomerisation
The MLIP reports the activation energy barrier for the forward reaction as 187 kJ/mol. This matches the literature benchmarked value which lies in the range of 180 kJ/mol - 190 kJ/mol.
Metadynamics Run